## Slide 1: Watt?
Smart Home Energy Conservation System

## Slide 2: Introduction
Introduction to IoT and connected devices
Remotely controllable and data accessible anywhere
Watt? Is simple IoT Application
Watt? Components
  Watt? Smart Meter
  Watt? Smart Plug
  Watt? Application

## Slide 3: Introduction

## Slide 4: Introduction
Advantages of IOT
  Communication
  Automation and Control
  Information
  Monitor
  Money

## Slide 5: Introduction
Internet of Things Architecture
Notes: Computing Environment [ESP8266]-
GPIO [Digital and Analog]

## Slide 6: Sensing Layer : Introduction
IoT is a set of sprawling technologies [cloud - Internet - Microprocessor]
Three major components of any IoT application :
  Device
  Gateway
  Cloud

## Slide 7: Sensing Layer : Introduction
Device is an embedded system
Characteristics of Embedded Systems:
  Single Functioned
  Tightly Constrained
  Reactive and Realtime
  Connected Hardware/Software systems
Notes:   Single Functioned [Measuring power and energy consumption of home and control appliances]
  Tightly Constrained [Cost - Size - Power - Performance]
  Connected [connected to peripherals]
  Hardware/Software systems [software for feature flexibility & Hardware for performance]

## Slide 8: Sensing Layer : Introduction
There are :
Diverse Hardware.
Diverse Software and Operating Systems.
Different Networking Protocols.

## Slide 9: Sensing Layer : Introduction
General Consideration when choosing hardware
Cost.
I/O Roles.
Power consumption.
Networking Environment.
Notes: I/O Roles [ADC for analog sensingPWM - Actuators].
Networking Environment [Ethernet - Wireless - cellular].

## Slide 10: Sensing Layer : Hardware
Infrastructure Components
Microcontroller [ESP8266]
32-bit RISC CPU: Tensilica Xtensa L106 running at 80 MHz
64 KiB of instruction RAM, 96 KiB of data RAM
External QSPI flash: 512 KiB to 4 MiB (up to 16 MiB is supported)
IEEE 802.11 b/g/n WiFi .
Integrated TR switch, balun, LNA, power amplifier and matching network .
WEP or WPA/WPA2 authentication, or open networks.
16 GPIO pins.
SPI.
I²C - I²S interfaces with DMA (sharing pins with GPIO).
UART on dedicated pins, plus a transmit-only UART can be enabled on GPIO2 10-bit ADC (this is a Successive Approximation ADC).
Memory: 4MB external EEPROM.
Communication: WiFi

## Slide 11: Sensing Layer : Hardware
Power supply components
  Electricity Network
    Hi-Link HLK-PM01 AC/DC Module
  Voltage regulator
    LM1117 LDO 3.3V-
Sensors
  Current Transformer
  ACS712 Current sensor IC - ACS712-20A Current sensor module.
Control Circuit
  ST Microelectronics's BTA16 Triac

## Slide 12: Sensing Layer : Hardware
PCB Design and Layout
  PCB design using EDA software
  PCB Layout and component placing
  PCB Production capabilities
  PCB Manufacturing challenges
    High Cost by the local manufacturers in Egypt.
    No high quality manufacturers found in Egypt.
    High customs if manufactured abroad in china.
    Preventing the manufactured products to arrive, from the national security in Egypt.
    Take long time to arrive if manufactured abroad.
    Bad quality of hand-made PCBs.
    Bigger size when manufactured in home.

## Slide 13: Sensing Layer : Software
The IoT Software Stack
  IoT Operating system .
  Hardware Abstraction Layer .
  Communication Support.
  Remote management.
Software architectures for Embedded Systems
  Round robin.
  Round robin with interrupts.
  Function queue scheduling.
  Realtime operating systems

## Slide 14: Embedded Software
Watt? Software architecture
Computing Environment
Hardware Interfaces
  GPIO
  UART
Notes: Computing Environment [ESP8266]-
GPIO [Digital and Analog]

## Slide 15: Sensing Layer : Software
On-device processing
  Converting data from ADC output format to a typical current value
  Calculating the Realtime power consumption.
  Validating data to ensure it meets a set of rules.
  Handling the external interrupts.
  Reading the Internet time.
  Calculating the cumulative energy consumptions.
  Storing data in the EEPROM.
  Combining data into aggregate values

## Slide 16: Network Layer
IoT Network Protocol Stack

## Slide 17: Network Layer
Watt? Networking
  Low power WiFi.
  Why WiFi ?
  Internet connection.

## Slide 18: Cloud Layer : Watt? Database
Entity Relationship Diagram

## Slide 19: Cloud Layer : Watt? Database
Tree Diagram
  User Tree

## Slide 20: Cloud Layer : Watt? Database
Tree Diagram
  Homes Tree

## Slide 21: Cloud Layer : Watt? Database
Tree Diagram
  Devices Tree

## Slide 22: Cloud Layer : Watt? Database
Relations
  Belongs To

## Slide 23: Cloud Layer : Watt? Database
Relations
  Has